## Slide 1
Aerodynamics
Angle A is called the angle of _________.
FAA-H-8083-25
A
Q

## Slide 2
Aerodynamics
Angle A is called the angle of incidence.
It is defined as the angle between the wing’s chord line and the aircraft’s longitudinal axis.
A

## Slide 3
Aerodynamics
Wingtip vortices are generated only when the wing is ___________.
FAA-H-8083-25
Q

## Slide 4
Generating lift.
Aerodynamics

## Slide 5
Aerodynamics
How many Gs you must pull in order to fly a level turn with 45 degrees of bank?
Q

## Slide 6
Cos  = Adj / Hyp
Cos 45 = 1 / X
X = 1/Cos 45
X = 1.41
Trigonometry tells us you must pull 1.4 Gs to fly a level, 45 degree banked turn.
Aerodynamics
1.4g
1.0g
1.0g
This tells us that, while performing steep turns, we should feel 41% heavier in the seat. You can incorporate this into your steep turn “crosscheck.”

## Slide 7
What two things are needed for a spin?
Aerodynamics
Q

## Slide 8
Stall and yaw.
The yaw is often referred to as “adverse yaw.”
Aerodynamics
Spin Video

## Slide 9
What factors cause a single engine, propeller driven airplane, to turn left?
FAA-H-8083-25B, Ch 5
Aerodynamics
Q

## Slide 10
P-Factor
Torque
Gyroscopic Precession
Spiraling Slip Stream (propwash)
Aerodynamics

## Slide 11
What is angle A called?
FAA-H-8083-25
A
Relative Wind
Aerodynamics
Q

## Slide 12
Angle a is called Angle of Attack.
Aerodynamics
A
Relative Wind

## Slide 13
True or False. An increase in gross weight will increase an aircraft’s critical angle of attack (AOA).
Aerodynamics
Q

## Slide 14
False.
A specific aircraft’s critical AOA never changes.
An increase in gross weight will, however, increase stall speed.
Note: most GA aircraft have a critical AOA of about 20 degrees.
Aerodynamics

## Slide 15
What is the positive G limit for a typical acrobatic category aircraft?
Aerodynamics
Q

## Slide 16
6 Gs
Aerodynamics

## Slide 17
What determines the longitudinal stability of an aircraft?
FAA-H-8083-25
Aerodynamics
Q

## Slide 18
The center of gravity relative to center of lift.
If the center of gravity is aft of the center of lift, the aircraft will be inherently unstable.
Aerodynamics

## Slide 19
During a spin to the left, which wing is stalled?
Aerodynamics
Q

## Slide 20
Both wings are stalled.
Aerodynamics

## Slide 21
What force causes an airplane to turn?
Aerodynamics
Q

## Slide 22
The horizontal component of the lift vector is what causes an airplane to turn.
Aerodynamics
Lift Vector
Horizontal Component
Vertical Component

## Slide 23
As airspeed decreases, what type of drag increases?
Assume you are maintaining level flight.
Aerodynamics
Q

## Slide 24
Induced drag increases when airspeed decreases.
To maintain level flight as airspeed decreases, we must increase our AOA. As AOA increases, our induced drag increases.
Aerodynamics

## Slide 25
What is camber angle?
FAA-H-8083-25
Aerodynamics
Q

## Slide 26
Layman’s terms: it is the curvature of the wing.
Varsity Level: It is the angle between a fixed horizontal reference line and a line drawn from the most forward leading edge of the wing to the most trailing edge of the wing. We can change camber angle by lower flaps or extending slats.
Aerodynamics

## Slide 27
If you plot total drag (induced drag plus parasitic drag) versus airspeed on a graph, the airspeed on the graph where the drag is the lowest is called____________ .
FAA-H-8083-3
Aerodynamics
Q

## Slide 28
Vg or Best Glide
Varsity Level: Vg is also known as L/Dmax (lift over drag maximum). This is often pronounced as “ L over D max.”
L/Dmax is also known as Max Range airspeed. It gives us the maximum range travelled with the minimum altitude lost.
Vg
Best Glide
L/Dmax
Aerodynamics
Lowest Total Drag

## Slide 29
When the velocity of a fluid increases, its pressure __________.
Aerodynamics
Q

## Slide 30
Decreases.
Known as Bernoulli's Principle. This is the principle behind how a wing generates lift and one of the contributing factors that lead to carb icing.
Aerodynamics

## Slide 31
What is Vy?
Aerodynamics
Q

## Slide 32
Vy is Best Rate of Climb Speed.
It is the airspeed where the greatest amount of excess power is available over that required for level flight. Vy will produce the most gain in altitude in the least amount of time (maximum rate of climb in feet per minute). Any attempts to obtain better climb performance by increasing pitch attitude will result in a decrease in climb rate.
Aerodynamics

## Slide 33
What is wing dihedral?
Aerodynamics
Q

## Slide 34
A design in which the wings slope upwards from the root. This design makes for a stable platform and tends to upright itself.
Dihedral
No Dihedral
Aerodynamics
Anhedral

## Slide 35
What part of the wing stalls first?
Why?
Aerodynamics
Q

## Slide 36
The wing roots stall first. We do not want the stall to occur instantly across the whole wing. We want it to progress slowly along the wing. We start at the root so the stall will have less tendency to roll the aircraft. Additionally, a stall occurring at the root first will be felt across the horizontal stabilizer and thus provide impending stall indications to the pilot.
Aerodynamics
Wing Roots

## Slide 37
What are the four dynamic forces that act upon an airplane during all phases of flight?
Aerodynamics
Q

## Slide 38
Lift, Weight, Thrust, and Drag.
Aerodynamics

## Slide 39
When does a stall occur?
Aerodynamics
Q

## Slide 40
When the critical angle of attack is exceeded.
Aerodynamics

## Slide 41
An airfoil passing through a fluid of greater density will produce greater ________.
Aerodynamics
Q

## Slide 42
Lift.
The denser the fluid, the more lift that is generated. Example, a specific wing flying at 10,000 ft density altitude will produce less lift than if it were flying at 5,000 ft density altitude. Another example would be a hydrofoil. When moving through water, it produces enough lift to raise a boat but produces almost no lift when moving through air.
Aerodynamics

## Slide 43
Give me a layman’s version of the formula for lift.
Q
Aerodynamics

## Slide 44
Total Lift SA + CA + AOA + AS + r
The lift generated by the wing is a function of the wing’s surface area (SA), camber angle (CA) , angle of attack (AOA), the aircraft’s airspeed (AS), and the density (r) of the fluid through which the airfoil is passing.
Aerodynamics

## Slide 45
What is Vx?
What circumstances would necessitate the use of Vx?
Aerodynamics
Q

## Slide 46
Vx – Best Angle of Climb Speed - Most altitude gained per distance travelled.
We typically use Vx when we need to cross obstacles or terrain after takeoff.
Aerodynamics

## Slide 47
As density altitude increases, Vx will __________.
Aerodynamics
Q

## Slide 48
Increase.
Side note: as DA increases, Vy will decrease. As DA increases, these two lines will move closer together. In theory, when they meet, the aircraft has reached its absolute service ceiling.
Aerodynamics
Vy
Vx
L/Dmax

## Slide 49
Vy
Here is a typical plot of the total drag curve for a given airplane. Where on this plot would you find Vx?
Aerodynamics
Q

## Slide 50
The bottom of the curve is called L/Dmax (pronounced “L over D max”). Vx is as far to the left of L/Dmax as Vy is to the right. In fact, (Vy-Vx)/2 +Vx is usually a pretty good estimate of L/Dmax. This is also Vg.
Aerodynamics
Vy
Vx
L/Dmax
Vg

## Slide 51
What effect does a forward center of gravity have on an aircraft's flight characteristics?
FAA-H-8083-1
Aerodynamics
Q

## Slide 52
Higher stall speed - critical angle of attack is reached at a higher speed due to increased wing loading.
Slower cruise speed - increased induced drag; greater angle of attack is required to maintain altitude.
More stable - the center of gravity is farther forward from the center of pressure which increases longitudinal stability.
Greater back elevator pressure required.
Longer takeoff roll.
Higher approach speeds.
Aerodynamics

## Slide 53
Name some factors that affect stall speed?
FAA-H-8083-25B. Ch 5
Aerodynamics
Q

## Slide 54
Gross weight, Load Factor (Gs), Bank Angle, Wing Configuration (flaps, slats, etc).
Aerodynamics

## Slide 55
You are in a steady-state climb at 300 fpm. Are all four forces (lift, weight, drag, thrust) in balance?
Aerodynamics
Q

## Slide 56
Yes.
A change in acceleration means a change in force (F=mA). If acceleration is zero, then there is no change in the force. In the example given, everything is in steady state therefore, no change in forces…in other words, they are all in balance.
Aerodynamics

## Slide 57
What is the purpose of flaps?
Aerodynamics
Q

## Slide 58
Flaps allow you to reduce airspeed and maintain the same amount of desired lift. This allows for slower takeoff and approach speeds all the while generating enough lift to fly.
Note: the purpose of flaps is not to let you fly a steeper approach. This is a second order effect of flaps but it is not the purpose of flaps.
Aerodynamics

## Slide 59
If your wing stalls at 19 degrees AOA, at what AOA is your wing producing the maximum possible lift?
Aerodynamics
Q

## Slide 60
Mathematically, your maximum lift would occur at 18.99999 degrees. However, this is impossible to see in the cockpit. So flying a few degrees less than critical AOA will maximize your wing’s performance. In most general aviation aircraft, you can identify it by keeping your AOA just out of the stall warning horn. More advanced aircraft will often have an AOA gauge.
Remember, during stall recoveries, you need a safe trade off between attaining safe flying airspeed and at the same time max performing your wing.
Aerodynamics

## Slide 61
How does density altitude affect aircraft performance?
Aerodynamics
Q

## Slide 62
Engine Performance (a 3% reduction in HP for each 1,000 ft increase in DA).
Reduced Lift Generated by the Wings (lift equation).
Reduced Thrust Generated by the propeller (a spinning wing).
Increased true airspeed for a given fixed indicated airspeed (leads to larger turn radius).
Increased ground speed for a given fixed indicated airspeed.
Aerodynamics

## Slide 63
There are many accidents in which an aircraft lifted off the runway and was able to climb when below takeoff speed. However, moments later, it began descending at a rate at which the pilot could not control. What do you think happened in these cases?
FAA-H-8083-25B, Ch 5
Aerodynamics
Q

## Slide 64
Ground effect. The aircraft lifted off and climbed due to ground effect. Once it climbed out of ground effect, it began descending. This descent cannot be stopped and they are already well past the departure end of the runway. Additionally, ground effect reduces induced drag which in turn provides excess thrust for acceleration. This often tricks pilots into thinking all is well. Here is an article on ground effect and a video of the potential dangers of ground effect.
Aerodynamics
Article
Video

## Slide 65
You are planning a cross country with a friend. She recommends moving the 25 pounds of luggage in the rear seats to the aft luggage compartment. The calculated CG is fine. Why would your friend recommend this?
FAA-H-8083-25B, Ch 4
Aerodynamics
Q

## Slide 66
This moves the CG aft which in turn results in a faster cruise speed and lower fuel consumption.
Aerodynamics

## Slide 67
As airspeed increases _________ drag increases.
FAA-H-8083-25, Ch 5
Aerodynamics
Q

## Slide 68
Parasitic drag.
Parasitic drag is created by things hanging out in the slipstream such as landing gear, antennas, rivets, etc. and is proportional to the square of the airspeed (this is why the drag graph is curved).
Example: hold your hand out your car window. As the car speeds up, the force pushing against your hand increases.
There is a speed at which an aircraft’s total (parasitic plus induced) drag is equal to its total thrust. This speed is the maximum speed the aircraft can fly (not withstanding other limitations such as Vne, over speeding the gear, etc.)
Aerodynamics

## Slide 69
At what height is ground effect more pronounced?
FAA-H-8083-3C, Ch 3
Aerodynamics
Q

## Slide 70
When within one wingspan or less from the ground.
At one half wingspan, induced drag is reduced by 25%. At one tenth of a wingspan, induced drag is reduced by as much as 50%.
Aerodynamics

## Slide 71
You are about to go out and do some spin training in your spin certified aircraft. You notice a few items in the aft luggage compartment. They are not needed for the flight. Should you remove them or leave them there?
Aerodynamics
Q

## Slide 72
As always, refer to your POH/AFM but generally speaking, during any acrobatics or spins, you want as much forward CG as possible. Remember, a forward CG is more stable and recovers easier in the event of an out of control situation. So, unless there is an overriding factor, you should either remove them or at least move them forward. Be sure they are secured!
Aerodynamics