## Slide 1
General Knowledge
Describe four classifications of NOTAMs.
Q

## Slide 2
General Knowledge
NOTAM (D) – “Distance Dissemination” NOTAMs. NOTAMs that affect public use airfields and navigational facilities in the NAS.
FDC NOTAMs – Flight Data Center NOTAMs. NOTAMs that are regulatory in nature including changes/updates to approaches, WAAS, or GPS service issues and TFRs. FDC NOTAMs are released by the servicing ARTCC.
Military NOTAMs – Issued by the military and usually limited to military use only airfields or NAVAIDs.
International NOTAMs – NOTAMs covering more than one country and issued in an ICAO format.
Note: The AIM sometimes labels the category as ‘Domestic (NOTAM D),’ but the ‘D’ means Distant, per FAA glossary/NOTAM page/PHAK.

## Slide 3
Unless otherwise published, how many Gs (positive and negative) can an aircraft in the “Utility” category normally pull?
Q
General Knowledge

## Slide 4
Maximum of…
+ 4.4 and -1.76
General Knowledge

## Slide 5
General Knowledge
How many types of airworthiness directives are there and what are they?
Q

## Slide 6
General Knowledge
There are three types of ADs.
Emergency – These require immediate compliance before flight.
One Time – After the AD is complied with once, there is no further need to address the specified issue.
Recurring – This AD must be complied with at the specified interval.

## Slide 7
General Knowledge
You use Basic Med. How often do you need to complete the online medical education course?
Q

## Slide 8
General Knowledge
Every two years.

## Slide 9
General Knowledge
You become lost while flying a cross country. What procedures will you follow (hint: The Five Cs)?
Q

## Slide 10
General Knowledge
The Five Cs.
Confess – Yep, I’m lost. (usually the hardest step)
Climb – See landmarks better. ATC can see you better. Better NAVAID reception.
Conserve – Slow down to save fuel (Vg is a good airspeed).
Communicate – Let someone know you are lost (ATC).
Comply – Comply with their instructions.
If you are flying at night in high terrain, you may consider adding a sixth C; “Circle”

## Slide 11
General Knowledge
What is True Airspeed?
14 CFR 1.1
Q

## Slide 12
General Knowledge
It is Equivalent Airspeed adjusted for temperature and pressure altitude.
Varsity Level: Since most GA aircraft are relatively slow, the compressibility of air is a non-factor. Therefore, some accept “True airspeed is calibrated airspeed adjusted for temperature and pressure altitude.”

## Slide 13
General Knowledge
What are the primary flight controls?
Q

## Slide 14
General Knowledge
Ailerons, rudder, elevator (or stabilator).

## Slide 15
General Knowledge
You want to turn on the runway lights at an uncontrolled airfield. To turn them on at medium intensity, you must click your mic button ______ times within ______ seconds.
AIM Table 2-1-3
How long will the lights stay on?
AIM 2-1-8
Q

## Slide 16
General Knowledge
For medium intensity, you must click the mic button 5 times within a 5 second period.
15 minutes.

## Slide 17
General Knowledge
What is Vfe?
Q

## Slide 18
General Knowledge
Maximum flap extension airspeed.

## Slide 19
General Knowledge
The Private Pilot ACS parameters for slow flight are________.
Q

## Slide 20
General Knowledge
Establish an altitude above 1,500 AGL
Heading +/- 10 degrees
Altitude +/- 100 feet
Airspeed +/- 10 kts
Bank +/- 10 degrees

## Slide 21
General Knowledge
You fly under Basic Med. How often do you need to have a comprehensive medical exam?
Q

## Slide 22
General Knowledge
Every four years.

## Slide 23
General Knowledge
You are on a Basic Med medical certificate and just bought an aircraft with a top speed of 325 knots. Can you fly this aircraft under Basic Med?
Q

## Slide 24
General Knowledge
Yes.
The 250 kt limit is a pilot limit, not an aircraft limit. So, you can continue escaping the bonds Earth but you have to do so below 250 kts.

## Slide 25
General Knowledge
You encounter turbulence during your cross country. Which is your priority?
Flying a constant airspeed and altitude
or
flying a straight and level attitude?
Q

## Slide 26
General Knowledge
Just do your best to fly a straight and level attitude. If ATC assigned you a specific altitude, tell them “unable” or request a block altitude such as “Request block 4 to 5.” (4,000 – 5,000 MSL)
Don’t “chase airspeed and altitude” when flying through turbulence.
Slow down below Va.

## Slide 27
General Knowledge
True or False. For weight and balance purposes, an aircraft’s BEW (basic empty weight) assumes all fuel tanks are full.
Q

## Slide 28
General Knowledge
False.
BEW assumes fuel tanks are empty and only the unusable fuel remains in the aircraft. Note: be sure to refer to your W&B section of the POH for any specifics regarding BEW.

## Slide 29
General Knowledge
What is the lowest altitude an aircraft may be operated over an area designated as a U.S. wildlife refuge, park, or Forest Service Area?
AIM 7-4-6
Q

## Slide 30
General Knowledge
All aircraft are requested to maintain a minimum altitude of 2,000 ft above the surface.
Notice it says “requested?” So, do your best to stay above 2,000 AGL.
Areas we are requested to fly over at a minimum of 2,000 ft AGL over the following areas:
National Parks
Monuments
Seashores
Lakeshores
Recreation Areas
Scenic Riverways
National Wildlife Refuges
Wilderness and Primitive Areas administered by the U.S. Forest Service, U.S. Fish and Wildlife Service, and National Park Service

## Slide 31
General Knowledge
What color is 100 LL aviation grade gasoline?
Q

## Slide 32
General Knowledge
Blue.

## Slide 33
General Knowledge
During stall practice, you must recover at or above what altitude ________ if single engine or ________ if multi engine.
Q

## Slide 34
General Knowledge
1,500 AGL single engine.
3,000 AGL multi-engine.

## Slide 35
General Knowledge
What is Basic Med?
Q

## Slide 36
General Knowledge
Basic Med is a way to fly without an FAA Medical Certificate. A Basic Med holder must have held an FAA medical certificate sometime in the past, take an online course every two years, fill out the FAA survey, and receive a medical exam from a state licensed doctor every 4 years.

## Slide 37
The red line on the airspeed indicator indicates what?
General Knowledge
Q

## Slide 38
Vne – Never exceed speed.
For multi-engine aircraft, another red line represents Vmc – minimal controllable airspeed.
General Knowledge

## Slide 39
A standard rate turn is a turn in which a 180-degree turn requires ______ minutes.
General Knowledge
Q

## Slide 40
One minute.
General Knowledge

## Slide 41
When is wake turbulence the strongest?
AIM 7-3-6
General Knowledge
Q

## Slide 42
When the aircraft generating the turbulence is heavy, clean, and slow.
When AOA is higher, the wake turbulence is greatest.
Heavier – A higher AOA is needed to generate the same amount of lift for a given airspeed.
Clean – If flaps are not used, a higher AOA is needed for a given airspeed.
Slow – The slower an airplane flies, the higher the AOA must be to generate the same amount of needed lift.
General Knowledge

## Slide 43
When is P-Factor the strongest?
FAA-H-8083-25B, Pg 5-32
General Knowledge
Q

## Slide 44
High power settings coupled with high AOA.
General Knowledge

## Slide 45
You are performing ground visual reference maneuvers. What are the checkride standards for the maneuvers?
General Knowledge
Q

## Slide 46
Altitude +/- 100 feet
Airspeed +/- 10 kts
Perform the maneuver at 600 – 1,000 feet AGL
General Knowledge

## Slide 47
The private pilot checkride standards for a short field landing state you must land within how many feet of your intended touchdown point?
Q
General Knowledge

## Slide 48
Zero feet short.
200 feet long.
General Knowledge

## Slide 49
What is magnetic variation?
FAA-H-8083-25B, Ch 8
General Knowledge
Q

## Slide 50
General Knowledge
Magnetic variation (also called magnetic declination) is the angle between true north and magnetic north.
It represents the difference between the direction of the geographic North Pole and the magnetic North Pole at a given location on Earth.

## Slide 51
Unless otherwise published how many Gs (positive or negative) can an aircraft in the “Normal” category normally pull?
Q
General Knowledge

## Slide 52
General Knowledge
Maximum of…
+ 3.8 and -1.52

## Slide 53
General Knowledge
What is calibrated airspeed?
Unless specifically published in your aircraft’s performance data, how can you calculate calibrated airspeed?
14 CFR 1.2
Q

## Slide 54
Indicated airspeed corrected for installation error.
The dynamic pressure sensed at the pitot tube/blade is transferred through a tube that goes to your airspeed indicator. As the tube snakes around through the wing, fuselage, and eventually reaches the airspeed indicator, some of that pressure is lost. This results in an indicated airspeed that is actually less than then actual airspeed sensed by the pitot tube/blade.
If not published, you can add 3kts.
In other words, to convert 100 KIAS to KCAS, add 3kts.
100 KIAS + 3kts = 103 KCAS
General Knowledge

## Slide 55
General Knowledge
The Private Pilot ACS parameters for steep turns are________.
Q

## Slide 56
General Knowledge
Bank approximately 45 degrees
Altitude +/- 100 feet
Airspeed +/- 10 kts
Bank +/- 5 degrees
Rollout heading +/- 10 degrees

## Slide 57
What is hypoxic hypoxia?
AIM 8-1-2
General Knowledge
Q

## Slide 58
It is a type of hypoxia caused by a low amount of oxygen in the blood. High altitude typically causes hypoxic hypoxia. This is the most common form of hypoxia.
General Knowledge

## Slide 59
How do you convert a true course to a magnetic heading?
General Knowledge
Q

## Slide 60
Either add a westerly variation to your true course or subtract an easterly variation from your true course. Remember “East is Least. West is Best.”
General Knowledge

## Slide 61
What are the typical spin recovery procedures?
General Knowledge
Q

## Slide 62
Power – Idle (reduces the load on the engine and reduces the aircraft’s left turning tendencies).
Ailerons – Neutral (anything other than neutral will “aggravate” the spin and delay recovery.
Rudder – Full opposite direction of spin (you need yaw and stall for a spin, this removes the yaw).
Elevator – Forward (reduces AOA so as to break the stall)
Recover from the Dive (yep, you’re now pointed at the ground).
Be sure to refer to your specific POH/AFM.
General Knowledge

## Slide 63
Define the term “Maneuvering Speed.”
FAA-H-8083-25C, Chapter 5, Pg 5-35
General Knowledge
Q

## Slide 64
Maneuvering speed is the max speed at which abrupt control movement can be applied or at which the airplane could be flown in turbulence without exceeding the design load factor limits. When operating below Va, a damaging positive flight load cannot be reached because the wing will stall before reaching that load factor (G forces).
General Knowledge

## Slide 65
What is a good rule of thumb for takeoff abort criteria?
General Knowledge
Q

## Slide 66
You should abort if you have not reached 70% of your takeoff speed by 50% of the runway.
General Knowledge

## Slide 67
What causes carb icing?
General Knowledge
Q

## Slide 68
A venturi within the carb causes a velocity increase in the fuel/air mixture. An increase in velocity creates a drop in pressure. A drop in pressure creates a drop in temperature. The temperature drop can be significant enough to cause moisture in the fuel/air mixture to freeze and adhere to the sides of the carburetor’s interior.
General Knowledge

## Slide 69
Why do we turn on carb heat during an air start after an engine failure?
General Knowledge
Q

## Slide 70
Provides an alternate air source for the engine.
It is not to remove carb icing. There is almost no heat left in the exhaust pipes of a dead engine moving through cold air at best glide airspeed.
General Knowledge

## Slide 71
What is the VHF emergency frequency?
General Knowledge
What is the UHF emergency frequency?
Q
AIM 6-2-4

## Slide 72
VHF - 121.5
UHF - 243.0
General Knowledge

## Slide 73
You determine you blew a tire during your takeoff roll and are now airborne. What are your actions?
Q
General Knowledge

## Slide 74
Follow the guidance in the AFM/POH. If there is none, consider the following:
- Do not retract flaps
- Do not retract gear
- Do not overspeed flaps or gear
- Divert to a runway that is longer and wider and minimal crosswind
- Burn down gas to lower gross weight
- During approach and touchdown, offset left or right so as to place the blown tire near the middle of the runway (drag in the middle)
- Use differential braking and nosewheel steering for directional control
- Stop straight ahead and do not taxi clear
General Knowledge

## Slide 75
General Knowledge
You landed at 12 noon, on time, and a friend picked you up at the airport. You forgot to close your VFR flight plan. When will your phone ring?
AIM 5-1-14
Q

## Slide 76
General Knowledge
It’ll probably start ringing around 12:30. Search and rescue efforts begin 30 minutes after your ETA if you do not close your flight plan. From the AIM:
“If a VFR flight plan is not closed, search and rescue procedures are started 30 minutes after the estimated time of arrival.”

## Slide 77
General Knowledge
What are LAHSO operations?
AIM 4-3-11
Q

## Slide 78
General Knowledge
LAHSO is an acronym for "land and hold short operations." Tower may clear a pilot to land and hold short of an intersecting runway, an intersecting taxiway, or some other designated point along the runway. Pilots may accept this clearance provided they determine the aircraft can safely land and stop within the available landing distance. Student pilots or pilots not familiar with the LAHSO should not participate in the program. Pilots are expected to decline if it is unsafe or weather is below basic VFR (a minimum of 1,000 feet and 3 miles visibility).

## Slide 79
You’ve achieved your goal of becoming a pilot and are flying the perfect cross country to a fairly busy airport. After landing, ground gives you confusing taxi instructions. Even after they repeat the instructions, you are still not sure what they want. Just to be safe and to ensure you follow their instructions, you can request a _____________.
Q
General Knowledge

## Slide 80
“Progressive taxi.” The radio call is pretty simple, “Ground, N777SS, request progressive.” Ground will tell you taxi straight ahead, turn left next taxiway, taxi straight ahead, turn right next taxiway, etc. as required to get you where you want to go. There’s no shame in requesting a progressive. With 30 years of flying experience, I still ask for one now and then!
General Knowledge

## Slide 81
What color is 100 aviation grade gasoline?
Q
General Knowledge

## Slide 82
Green.
General Knowledge
Yep, you probably answered blue. Notice the question didn’t ask about 100 LL. It asked about 100.