## Slide 1
Navigation
What is the first step when proceeding direct to a VOR?
Q

## Slide 2
Navigation
Tune, Identify, and Monitor the VOR.
T.I.M.
Tune the freq. Identify the station by listening to the morse code. Monitor it during use to ensure a valid signal.
You’ll do this a lot during your instrument training!

## Slide 3
Navigation
A typical floating type magnetic compass will operate correctly up to ____ degrees of bank and ____ of pitch.
FAA-H-8083-25B, Ch 8
Q

## Slide 4
Navigation
18 degrees of bank and 18 degrees of pitch.

## Slide 5
Navigation
What is magnetic deviation?
AIM 7-5-2
Q

## Slide 6
Navigation
Magnetic deviation is the error in a magnetic compass caused by magnetic fields within the aircraft itself.
Sources of aircraft deviation are electronics, metal, and electrical current flow. Your maintenance folks will taxi out to a “compass rose” painted on the ramp and point directly towards magnetic north. Then they’ll note what the magnetic compass reads and record the difference on a “deviation card” and post it in the cockpit.

## Slide 7
Navigation
You turn your OBS until the CDI is centered and notice a “TO” indication. Are you flying towards the VOR?
Q

## Slide 8
Navigation
Unless your heading is exactly equal to the top of what’s dialed into your OBS, the answer is no.
Your VOR nav instrument (sometimes the entire instrument itself is called an OBS as well as the knob) has no idea which way you are pointed much less if you are flying towards the station. The “TO” indication simply says, “If you intercept the radial you have dialed in the OBS you will be flying towards the VOR.”