## Slide 1
Systems
During your runup, you notice there is no RPM drop when the ignition switch is in LEFT. What is wrong?
FAA-H-8083-25
Q

## Slide 2
Systems
The right magneto P-lead (grounding wire) is disconnected or the right magneto has completely failed. When you move the ignition switch to LEFT, the right magneto should have grounded out.

## Slide 3
Systems
You are on a cross country flight and drop into an uncontrolled airfield. When you are ready to depart, you find the AWOS is out of service. What will you set your altimeter to?
Q

## Slide 4
Systems
You should adjust the altimeter setting until the altimeter reads the same as the field elevation.
If there is another altimeter setting available nearby you can use that one. Ideally, you want the source to be within at least 100 nm.

## Slide 5
Systems
On the traditional “six pack,” what are your pitot static instruments?
Q

## Slide 6
Systems
Altimeter
VVI (or VSI)
Airspeed Indicator
Did you notice something? On a traditional six pack, every instrument that has a needle is a pitot static instrument.

## Slide 7
Systems
On a traditional “six pack” layout, which of your flight instruments contain gyroscopes?
How are they powered?
Q

## Slide 8
Turn Rate Indicator – Electric Powered
Directional Gyro – Vacuum Powered
ADI – Vacuum Powered
Systems

## Slide 9
Why does carb heat/alternate air typically reduce power on the engine?
Systems
Q

## Slide 10
With carb heat on, the engine is drawing in warmer air. This is equivalent to operating at a higher density altitude. The amount of oxygen per cubic volume is reduced and, when warmer air is used, the mixture tends to be enrichened.
Many alternate air intakes are within the engine cowling and they therefore draw in air that is much warmer than the outside air.
Systems

## Slide 11
Systems
You have a fairly new ELT. When activated, what frequencies will it transmit on?
AIM 6-2-5
Q

## Slide 12
Systems
121.5 KHz (VHF)
243.0 KHz (UHF)
406 MHz (UHF)
Varsity Level: The 406 MHz frequency will be received by COSPAS-SARSAT satellites and in turn notify several national search and rescue centers. Additionally, if so programmed, the 406 MHz signal can contain personal information and contact information.

## Slide 13
Systems
What four strokes must occur in each cylinder of a typical four stroke engine in order for it to produce full power?
FAA-H-8083-25
Q

## Slide 14
Systems
INTAKE – the fuel/air mixture is drawn into the cylinder by the downward piston stroke.
COMPRESSION – the fuel/air mixture is compressed by the upward piston stroke.
POWER – the spark plug ignites the fuel/air mixture forcing the piston downward thus producing power.
EXHAUST – the burned gases are pushed out of cylinder by the upward piston stroke.

## Slide 15
Systems
What change occurs to the fuel/air mixture when applying carburetor heat?
FAA-H-8083-25
Q

## Slide 16
Systems
Using carb heat will normally enrichen the mixture.

## Slide 17
Systems
How many spark plugs are there per cylinder and why?
Q

## Slide 18
Systems
Two spark plugs per cylinder.
This provides redundancy and more efficient combustion – which leads to more power.
Watch what happens to your EGT during a mag check. See how EGT goes up? This is because combustion is still occurring with the exhaust gases as they pass through the exhaust system. This release of energy should be happening in the cylinder. But it’s not, so there is a loss of power – hence the drop in RPM.
Note: if your aircraft burns Jet-A or diesel fuel, you won’t have spark plugs.

## Slide 19
Systems
What is the voltage and amperage of your aircraft’s alternator?
Q

## Slide 20
Systems
Study your aircraft systems and know the answer for your specific aircraft. Typically, a small GA aircraft is 14 Volts and 60 Amps.

## Slide 21
Systems
What is your aircraft’s rated horsepower?
Q

## Slide 22
Systems
Study your aircraft systems and know the answer for your specific aircraft.

## Slide 23
Systems
What is “preignition?”
FAA-H-8083-25B, Ch 7
Q

## Slide 24
Systems
Pre-ignition occurs when the fuel air mixture ignites prior to the spark plug firing. This results in reduced engine power and high operating temperatures. Pre-ignition is usually caused by a residual hot spot in the combustion chamber, often created by a small carbon deposit on a spark plug, a cracked spark plug insulator, or other damage in the cylinder that causes a part to heat sufficiently to ignite the fuel air charge. Pre-ignition may cause severe engine damage because the expanding gases exert excessive pressure on the piston while still on its up stroke.

## Slide 25
Where does your carb heat get its heat?
Systems
Q

## Slide 26
Outside, unfiltered, air is drawn across the exhaust system and heated. It is then directed to the airbox and in turn to the carburetor. Normal filtered air is blocked when carb heat is on.
Systems

## Slide 27
Where does the power for engine ignition come from?
What happens to this source of power if you turn your master switch off?
Systems
Q

## Slide 28
From two magnetos.
Your aircraft’s master switch has no effect on the magnetos. They operate completely independent of the aircraft’s electrical system.
Systems

## Slide 29
What is an advantage of a constant speed propeller?
Systems
Q

## Slide 30
The pilot can select the most efficient propeller pitch for all phases of flight.
Systems

## Slide 31
You are flying an aircraft with a constant speed propeller. Your first engine instrument indication of carb icing will most likely be _____________.
Systems
Q

## Slide 32
A reduction in manifold pressure.
You might think the answer is RPM. But as horsepower decreases, the governor will adjust the propeller pitch to maintain the RPM selected by the RPM lever. So, your only real indication of a reduction in power is a reduction in manifold pressure.
Systems

## Slide 33
Systems
You have a 50 Amp hour battery.
You just experienced an alternator failure. How can you approximate the time remaining until complete electrical failure?
Q

## Slide 34
Systems
Note the amp rating on each of the circuit breakers for the equipment you have turned on/operating. Add them up. Then divide 50 by that number. This approximates the time (in hours) you have.
Example: you are drawing 35 amps. 50/35 = 1.4 You have approximately 1.4 hours of battery life.
Important: there will be systems drawing current from the battery for which you won't know the amperage. Some POHs/AFMs may have this data. In other words, the number you come up with is a rough approximation.
Additionally, most aircraft components won’t keep running until your battery is down to zero volts. Most will shutdown after a drop of only a few volts. In other words, 1.4-hour battery life doesn’t mean your aircraft components will operate for 1.4 hours.

## Slide 35
When is your magnetic compass the most accurate?
AIM 8-1-3
Systems
Q

## Slide 36
During straight and level, unaccelerated flight.
Systems

## Slide 37
The alternator’s (or generator’s) output voltage, if working properly, will be _______ than the battery voltage.
Systems
Q

## Slide 38
Higher.
To move voltage from source A to storage B, source A must be higher.
Much like water. To move water from a lake into a tank with a given back pressure, the water pressure from the lake must be great than the back pressure of the tank.
Systems

## Slide 39
Why do most small GA aircraft use alternators instead of generators?
FAA-H-8083-25B, Ch 7
Systems
Q

## Slide 40
Alternators weigh less.
Alternators are cheaper.
Alternators require less maintenance.
Alternators generate more current at lower RPM.
By the way, for these same reasons…your car has an alternator.
Systems